## Slide 1
SMARTPMS - DIGITAL QUALITY MAPS AS AID FOR
MAINTENANCE OF ROAD NETWORKS
SMARTPMS – KVALITETNE DIGITALNE KARTE KAO
POMOĆ U ODRŽAVANJU CESTOVNE MREŽE
DAVIDE LO PRESTI, UNIVERSITY PALERMO
davide.lopresti@unipa.it
smartilab.unipa.it
9. MEĐUNARODNA KONFERENCIJA ASFALTNI KOLNICI 2025
9. INTERNATIONAL CONFERENCE ASPHALT PAVEMENTS 2025
OPATIJA 08. – 09. 05. 2025.

## Slide 2
Engeneering sustainability in each stage of the life cycle of transport infrastructure
http://smartilab.unipa.it
in an oversimplified form can be summarised as the implementation of best practices deduced from the
Life Cycle Analsys (LCA) of projects, processes and products
Moins et al. 2020

## Slide 3: Sustainable Road Infrastructure: Definitions and Regulations
smartilab.unipa.it

## Slide 4
Engineering Sustainability in road infrastructure is a huge challenge that touches on many aspects and that
in an oversimplified form can be summarised as the implementation of best practices deduced from the
Life Cycle Analsys (LCA) of projects, processes and products
Moins et al. 2020
Intro: Sustainable Road pavements

## Slide 5
Green Public Procurement for roads GPP roads (EU, 2016)
1.3.1 The most significant environmental impacts of roads
The most significant environmental impacts derived from LCA studies
1) from daily traffic (fuel consumption of passenger cars and heavy trucks) during the road use phase.
Rolling resistance,
Congestion (traffic)
2) The production of materials
Extraction
Transport
Re-use/Recycling
Intro: Sustainable Road pavements

## Slide 6
Green Public Procurement for roads GPP roads (EU, 2016)
Intro: Sustainable Road pavements
1.3.1 The most significant environmental impacts of roads
Maintenance and rehabilitation... should not be considered as a simple repetition of rehabilitation and repair activities, but as a complex network of planning strategies, including the assessment of
rolling resistance,
congestion and
durability of road surface materials.
…therefore, when durable materials are used, the need for maintenance is reduced.

## Slide 7
Speed
Roughness (i.e IRI)
Problem 1: Emissions due to Rolling Resistance
«The IRI is based on the average rectified slope (ARS), which is a filtered ratio of a standard vehicle's accumulated suspension motion (in mm, inches, etc.) divided by the distance traveled by the vehicle during the measurement (km, mi, etc.). IRI is then equal to ARS multiplied by 1,000»
source: pavementinteractive.org
Intro: Sustainable Road pavements

## Slide 8
Problem 1: Emissions due to Rolling Resistance
Intro: Sustainable Road pavements

## Slide 9
Problem 2: Emissions due to maintenance-derived congestion: «planning/schedule» and «durability»
Intro: Sustainable Road pavements

## Slide 10
Source: https://doi.org/10.1016/j.autcon.2020.103336
Problem 1 and 2:
a solution: PMS!
Intro: Sustainable Road pavements

## Slide 11
Roughness evaluation using direct measurement equipment type (high to moderate cost)
Source: https://doi.org/10.3390/rs15112941
Problem 1 and 2: solved with PMS!
Intro: Sustainable Road pavements
Notes: riepilogo dei dispositivi di raccolta dei dati di rugosità più comunemente utilizzati, dei relativi principi di misurazione, dei costi, dei relativi gradi di accuratezza e dell'uso attuale e previsto per il futuro.

## Slide 12
Roughness evaluation using INdirect measurement equipment type (moderate to low cost)
Source: https://doi.org/10.3390/rs15112941
Problem 1 and 2: solved with PMS!
Intro: Sustainable Road pavements
Notes: riepilogo dei dispositivi di raccolta dei dati di rugosità più comunemente utilizzati, dei relativi principi di misurazione, dei costi, dei relativi gradi di accuratezza e dell'uso attuale e previsto per il futuro.

## Slide 13: SMARTPMS Urban: Why? How? What?
smartilab.unipa.it

## Slide 14
SMARTPMS – Why?

## Slide 15
CHATGPT Prompt:
ehi bot! ciao :)
can you please tell me the length in kms of national roads and local roads for the major european countries? please make a table and provide me with references
Great! can you please specify also the length. of road managed solely by local road authorities?
How big could be the problem of Urban roads in EU?
SMARTPMS – Why?
Notes: How about Urban roads in EU?

## Slide 16
Road Network Lengths by Country (in km)
Country | Motorways | National Roads | Secondary/Regional Roads | Local Roads (Managed by Local Authorities) | Total Road Network
France | 11,664 | 9,581 | 378,906 | 704,942 | 1,105,094
Germany | 13,155 | 37,824 | 178,622 | — | 229,601
Italy | 6,978 | 28,307 | 132,626 | 67,532 | 235,443
Spain | 15,860 | 14,880 | 134,945 | 501,053 | 666,738
United Kingdom | 3,764 | 49,215 | 369,535 | — | 422,514
Poland | 1,761 | 19,498 | 153,782 | 256,536 | 431,577
Netherlands | 2,790 | 2,743 | 7,905 | 127,804 | 141,242
Sweden | 2,185 | 13,497 | 141,187 | 43,156 | 200,025
Austria | 1,749 | 10,762 | 23,555 | 91,916 | 127,982
Belgium | 1,763 | 13,229 | 1,349 | 138,869 | 155,210
SMARTPMS – Why?

## Slide 17
Road Network Lengths by Country (in km)
Country | Motorways | National Roads | Secondary/Regional Roads | Local Roads (Managed by Local Authorities) | Total Road Network
France | 11,664 | 9,581 | 378,906 | 704,942 | 1,105,094
Germany | 13,155 | 37,824 | 178,622 | — | 229,601
Italy | 6,978 | 28,307 | 132,626 | 67,532 | 235,443
Spain | 15,860 | 14,880 | 134,945 | 501,053 | 666,738
United Kingdom | 3,764 | 49,215 | 369,535 | — | 422,514
Poland | 1,761 | 19,498 | 153,782 | 256,536 | 431,577
Netherlands | 2,790 | 2,743 | 7,905 | 127,804 | 141,242
Sweden | 2,185 | 13,497 | 141,187 | 43,156 | 200,025
Austria | 1,749 | 10,762 | 23,555 | 91,916 | 127,982
Belgium | 1,763 | 13,229 | 1,349 | 138,869 | 155,210
Notes:
Motorways: High-capacity roads designed for fast traffic, with controlled access and no at-grade crossings.
National Roads: Major roads connecting cities and regions.
Secondary/Regional Roads: Roads connecting smaller towns and localities.
Local Roads: Roads managed solely by local authorities, including municipal and communal roads.
Sources:
European Union Road Federation (ERF) - Road Network 2024: erf.be/statistics/road-network-2024
European Commission - Eurostat: ec.europa.eu/eurostat
Please note that definitions of road categories may vary between countries, and some data may be subject to updates. Let me know if you need more detailed information or data for other countries!
SMARTPMS – Why?

## Slide 18: How about Urban roads?
Country | Motorways | National Roads | Local Roads | Total Road Network | Local + Secondary %
France | 11,612 | 9,044 | 1,082,889 | 1,103,545 | 98,13%
Germany | 12,996 | 38,018 | 178,876 | 229,890 | 77,81%
Italy | 6,943 | 20,786 | 228,838 | 256,567 | 89,19%
Spain | 15,444 | 14,905 | 636,312 | 666,661 | 95,45%
United Kingdom | 3,764 | 49,215 | 369,535 | 422,514 | 87,46%
Poland | 1,640 | 1,425 | 402,893 | 405,958 | 99,24%
Netherlands | 2,758 | 2,627 | 134,305 | 139,690 | 96,15%
Sweden | 2,118 | 13,565 | 199,696 | 215,379 | 92,72%
Austria | 1,743 | 10,826 | 117,820 | 130,389 | 90,36%
Belgium | 1,763 | 13,229 | 140,218 | 155,210 | 90,34%
Road Network Lengths by Country (in km)
SMARTPMS- Background

## Slide 19
Road Network Lengths by Country (in km)
Country | Motorways | National Roads | Secondary/Regional Roads | Local Roads (Managed by Local Authorities) | Total Road Network | Local roads %
France | 11,664 | 9,581 | 378,906 | 704,942 | 1,105,094 | 63,79%
Germany | 13,155 | 37,824 | 178,622 | — | 229,601 | -
Italy | 6,978 | 28,307 | 132,626 | 67,532 | 235,443 | 28,68%
Spain | 15,860 | 14,880 | 134,945 | 501,053 | 666,738 | 75,15%
United Kingdom | 3,764 | 49,215 | 369,535 | — | 422,514 | -
Poland | 1,761 | 19,498 | 153,782 | 256,536 | 431,577 | 59,44%
Netherlands | 2,790 | 2,743 | 7,905 | 127,804 | 141,242 | 90,49%
Sweden | 2,185 | 13,497 | 141,187 | 43,156 | 200,025 | 21,58%
Austria | 1,749 | 10,762 | 23,555 | 91,916 | 127,982 | 71,82%
Belgium | 1,763 | 13,229 | 1,349 | 138,869 | 155,210 | 89,47%
SMARTPMS – Why?

## Slide 20
Real Time data from Connected Vehicles (CVs)
IoT (Internet of Things) and V2X (Vehicle-to-Everything) technologies enable frequent and distributed road network measurements.
Through our partner NiraDynamics, it is possible to access several type of data from a fleet of passenger vehicles
SMARTPMS – How

## Slide 21
Real Time data from Connected Vehicles (CVs)
SMARTPMS – How

## Slide 22
SMARTPMS – How

## Slide 23
Problem 1: Emissions due to maintenance derived congestion (traffic)
Intro: Sustainable Road pavements
Source: https://doi.org/10.1016/j.autcon.2021.103840

## Slide 24: SMART PMS Urban : CVs-derived urban digital quality maps for predictive maintenance of urban road networks
smartpms.unipa.it

## Slide 26
traditional reactive maintenance, characterised by interventions carried out only after a failure occurs,
    to proactive maintenance, based on regular inspections aimed at preventing failures:
      Historical data
      Quality maps of roughness
      PotHoles and Bumps mapping
      Road Health Alerts
CVs make maintenance model going from
SMARTPMS Urban – CV data

## Slide 27
SMARTPMS Urban – CV data
      Historical data
      Quality maps of roughness
      PotHoles and Bumps mapping
      Road Health Alerts

## Slide 28
SMARTPMS Urban – CV data
      Historical data
      Quality maps of roughness
      PotHoles and Bumps mapping
      Road Health Alerts

## Slide 29
SMARTPMS Urban – CV data
      Historical data
      Quality maps of roughness
      PotHoles and Bumps mapping
      Road Health Alerts

## Slide 30
traditional reactive maintenance, characterised by interventions carried out only after a failure occurs,
    to proactive maintenance, based on regular inspections aimed at preventing failures, and
          predictive maintenance, which integrates advanced monitoring techniques with predictive algorithms.
CV makes maintenance model going from
SMART PMS Urban
SMARTPMS Urban – the concept

## Slide 31
Data analysis
Decision making
Monitoring mixing CV and visual data
Type of maintenance | When | Goal
Reactive | After failure occurs | Fixing
Proactive | Before failure occurs | Road Alerts
Predictive | Predicted from hystorical data | Road manager predictions
SMARTPMS Urban – the concept

## Slide 33
SmartPMS is an integrated system designed to help urban road network managers allocate their budget based on the actual and predicted road conditions (based on Roughness).
These predictions are made possible by the large amount of data provided by Connected Vehicles and advanced Machine Learning models in a user-friendly private portal.
SMARTPMS Urban – the concept

## Slide 34
CV
Partners’ Databases
SmartPMS ML Framework
Filtering
Aggregation
ML Training
Prevision
SmartPMS Portal
Tools
Quality map
Intervention List
SMARTPMS Urban – the concept
Notes: The workflow pipeline includes:
  Data collection from Connected Vehicles’s databases
  Machine learning model training
  Publishing results to a private portal for the municipality
Using regression models enables accurate predictions while maintaining a low environmental impact due to reduced computational costs.

## Slide 35
One of the most important tools is dynamic mapping based on predicted data. These maps use a traffic light-style gradient to visualize the future evolution of road network conditions.
Palermo, Sicily (IT)
Tool 1: Dynamic Quality Maps

## Slide 36
Actual
Legenda
Ottima
Buona
Normale
Scarsa
Critica
Dati mancanti o non sufficienti
Quality maps

## Slide 37
Quality maps
Chart: Regressione lineare

## Slide 38
Legenda
Ottima
Buona
Normale
Scarsa
Critica
Dati mancanti o non sufficienti
Predicted (6,12,18,24 months)
Quality maps

## Slide 39
Decision making is supported by an algorithm that prioritizes based on predicted data over the next two years. This helps simplify budget allocation and planning.
Palermo, Sicily (IT)
Tool 1: priority list of interventions

## Slide 40: priority list of interventions
Condizione superficiale |  | ATTUALE | Lunghezza strada nel caso studio
 |  | Via (functional class 5) | 
CRITICA |  | Via Armò | 92.51 m
 |  | Via Pellegrino Raffaele | 62.22 m
 |  | Via Giuseppe Gentile | 119.08 m
 |  | Via Giuseppe Patricolo | 130.16 m
Condizione superficiale |  | PREVISTA(2 ANNI) | Lunghezza strada nel caso studio
 |  | Via (functional class 5) | 
CRITICA |  | Via de Borch | 142.51m
 |  | Via Armò | 92.51 m
 |  | Via Buccola | 155.77m
 |  | Via Niccolò Machiavelli | 124.48m
 |  | Via Andrea Chiaramonte | 352.27m
 |  | Via Pietro d'Aragona | 329.23m
 |  | Via Gaspare Palermo | 403.12m
 |  | Via Pellegrino Raffaele | 62.22 m
 |  | Via Giuseppe Gentile | 119.08 m
 |  | Via Giuseppe Patricolo | 130.16 m
 |  | Via Perni Francesco Maggiore | 172.99m
The graph takes into account the IRI distribution of the various sub-segments falling within the case study, the surface condition instead concerns the road after its aggregation

## Slide 41: priority list of interventions
Condizione superficiale |  | ATTUALE | Lunghezza strada nel caso studio
 |  | Via (functional class 5) | 
SCARSA |  | Via Liborio Giuffrè | 370.49 m
 |  | Via Paolo Emiliani Giudici | 472.07 m
 |  | Via Antonio Marinuzzi | 532.68 m
 |  | Via Filippo Corazza | 473 m
 |  | Via Mendola | 456.1 m
 |  | Via Buccola | 155.77m
 |  | Via Niccolò Machiavelli | 124.48m
 |  | Via Colomba | 215.9 m
 |  | Via Pietro d'Aragona | 329.23m
 |  | Via Monfenera | 95.9 m
 |  | Via Cosmo Guastella | 235.33 m
 |  | Via Virgilio La Scola | 59.5 m
 |  | Via Perni Francesco Maggiore | 172.99m
Condizione superficiale |  | PREVISTA(2 ANNI) | Lunghezza strada nel caso studio
 |  | Via (functional class 5) | 
SCARSA |  | Via Liborio Giuffrè | 370.49 m
 |  | Via Paolo Emiliani Giudici | 472.07 m
 |  | Via Antonio Marinuzzi | 532.68 m
 |  | Via Filippo Corazza | 473 m
 |  | Via Mendola | 456.1 m
 |  | Via Vincenzo Errante | 386.45 m
 |  | Via Salamone Marino Salvatore(fc5) | 315.48 m
 |  | Via Colomba | 215.9 m
 |  | Via Monfenera | 95.9 m
 |  | Via Cosmo Guastella | 235.33 m
 |  | Via Rocco Jemma | 76.41 m
 |  | Via Salvatore Morso | 156.12 m
 |  | Via Virgilio La Scola | 59.5 m
The graph takes into account the IRI distribution of the various sub-segments falling within the case study, the surface condition instead concerns the road after its aggregation

## Slide 42: priority list of interventions
Condizione superficiale |  | ATTUALE | Lunghezza strada nel caso studio
 |  | Via (functional class 5) | 
NORMALE |  | Via del Vespro | 741.42 m
 |  | Via Giorgio Arcoleo | 466.4 m
 |  | Via Vincenzo Errante | 386.45 m
 |  | Via de Borch | 142.51 m
 |  | Via Salamone Marino Salvatore(fc5) | 315.48 m
 |  | Via Andrea Chiaramonte | 352.27m
 |  | Via Alfonso Il Magnanimo | 95.35 m
 |  | via Filiciuzza | 229.24 m
 |  | Via Gaspare Palermo | 403.12m
 |  | Via Vito d'Ondes Reggio | 253.06 m
 |  | Via Augusto Elia | 188.32 m
 |  | Via Rocco Jemma | 76.41 m
 |  | Via Salvatore Morso | 156.12 m
 |  | Via Abele Aiello | 76.29 m
 |  | Via delle Cliniche | 149.52 m
Condizione superficiale |  | PREVISTA(2 ANNI) | Lunghezza strada nel caso studio
 |  | Via (functional class 5) | 
NORMALE |  | Via del Vespro | 741.42 m
 |  | Via Giorgio Arcoleo | 466.4 m
 |  | Via Alfonso Il Magnanimo | 95.35 m
 |  | via Filiciuzza | 229.24 m
 |  | Via Vito d'Ondes Reggio | 253.06 m
 |  | Via Augusto Elia | 188.32 m
 |  | Via Abele Aiello | 76.29 m
 |  | Via delle Cliniche | 149.52 m
The graph takes into account the IRI distribution of the various sub-segments falling within the case study, the surface condition instead concerns the road after its aggregation

## Slide 43
REDUCING CONGESTION WITH PLANNED MAINTENANCE
NO reactive maintenance! in favour of planned maintenance
Main roads: pro-active and predictive maintenance + network analysis (based on roughness and friction?)
Urban roads: predictive maintenance maintenance + network analysis (for each city area? For the whole city?)
and secondary roads?
  What if metropolitan cities were to have a Preventive Maintenance System, comparative and perhaps a reward system that would apply to ALL NETWORKS of the REGION?
Conclusions

## Slide 44
Our set of tools doesn’t stop here!
SMARTPMS is being currently developed with Palermo Municipality (first big city in EU?). We are actively seeking feedback and further collaborations to support municipalities in improving their budget forecasts and road infrastructure planning
SMARTPMS Urban – what’s next

## Slide 45
SMARTPMS- Background
08/05/2025
News!
Davide Lo Presti
Associate Professor University of Palermo (IT)
davide.lopresti@unipa.it
@SMARTIlab UNIPA
smartilab.unipa.it

## Slide 46
SMART solutions also….in education from 2026/2027
http://surpave.eu
Hvala!
see you in Palermo in October/November 2026
#ROADLCA2026
The research work has been supported by the European Union - NextGenerationEU - National Sustainable Mobility Center CN00000023, Italian Ministry of University and Research Decree n. 1033— 17/06/2022, Spoke 2, CUP B73C2200076000.